## Slide 1: Theme 6, Inland Waters - Highlights
SWOT data quality and first results on rivers and lakes
  Excellent data products on rivers and lakes, WSE better than W and S, still issues with dark water, bright land
  Hydraulic visibility improved by SWOT spatial coverage
  Accuracy of SWOT WSE at both node and reach scales: 10 cm during the cal/val phase. Detection of dams, locks, flow waves propagating
  Detect smaller scale changes in river slope compared to previous conventional missions
  Difference generally of around 10 cm and no clear bias with/without cross-over calibration over lakes
  Detection of ice breakups, melting and refreezing for lake ice and overlying snow properties
  The good, the bad, the ugly: discharge estimates are still a work in progress (in particular widths are still flawed)
  WSE on large lakes to be fully appreciated in the context of underlying geoid
Altimetry data processing on inland waters:
  Filtering out abnormal waveforms on L1 data to make the retracker work easier
  Shift towards space-time based methods on 2D radargrams for WSE retracking
  Use of Sentinel-6MF Fully Focused SAR for improved WSE retrieval and off-nadir virtual stations
Data assimilation in models
  Optimistic outlook for sub-weekly data assimilation of SWOT measurements at various basin scales
Use of altimetry in the context of WSE and discharge prediction
  Dense spatial sampling of geodetic missions is crucial to determining river hydraulics model parameters
  Extension of global GRDC discharge gauges using non-parametric functions from altimetric VS
  Autoregressive prediction model based on gauge data to predict at altimetry virtual stations
  Advantages of merging altimetry with optical imagery to improve rating curve discharge estimations
  Altimetry, in particular SWOT, can inform about seasonal and inter-seasonal water dynamics, especially in ungauged basins (e.g. Congo river basin)
Future missions:
  Sentinel-3 NGT 50 km swath, 5-day global revisit
  SMASH concept nadir altimeters, 200 km intertrack spacing and 1-day revisit at ~40,000 virtual stations
  SWOT LOAC: towards new physics to compute water velocity and surface topography with cross-track and along-track interferometry?

## Slide 2: Theme 6, Inland Waters - Recommendations
SWOT data quality and first results on rivers and lakes
  Further analysis of SWOT capacity over narrow rivers (between 30 and 60 meters)
  Study seasonal variations in slopes over the course of a year with a precision as never before
  Keep on improving river width estimations and validation of SWOT against in situ/other altimetry missions
  Processing of SWOT data to deal with dark water pixels, correction algorithm tailored for snow and ice conditions
  Correcting mean lake surface deformations on very large lakes before use
Altimetry data processing on inland waters:
  Further waveform filtering from L1A is recommended
  Use off-nadir measurements from FF-SAR
  Find a trade-off between improving retracking and revisiting the virtual station definition
  Collective work for historic WSE data collection over the past 30 years
Data assimilation in models
  Continue evaluating the trade-space for data assimilation (e.g. inflation, localization radius)
Use of altimetry in the context of WSE and discharge prediction
  More multi-mission studies over rivers.
  More studies on ungauged basins (e.g. Africa)
Future missions:
  Need of new missions (altimeter and multispectral) with improved spatial and temporal resolution; need to invest in machine learning to support the physical models
  Daily data (e.g. SMASH) would bring invaluable additional precision to data assimilation endeavors
  Continue dedicated investigations on the trade space for hypothetical observing systems
  Use of drones to bridge the gaps between ground truths and satellite data